## Slide 1: Introduction to ROS (Robot Operating System)
Jikai Wang

## Slide 2: What is ROS?
ROS (Robot Operating System) is an open source software development kit for robotics applications.
ROS offers a standard software platform to developers across industries that will carry them from research and prototyping all the way through to deployment and production.

## Slide 3: Why ROS?
Standardization:
  Offers a common platform for robotics research and development.
Flexibility:
  Supports a wide range of robot hardware and software.
Community:
  Large and active community contributing to its development and improvement.

## Slide 4: Key Features of ROS
Middleware:
  Facilitates communication between different components of a robot.
Reusable Code:
  Enables code sharing and reuse through a package system.
Simulation:
  Allows testing and development in virtual environments before deploying on actual robots.

## Slide 5: Robotics using ROS

## Slide 6: ROS Core Concepts
Nodes
Topics
Messages
Services

## Slide 7: ROS Nodes
Single-purposed executable programs
  e.g. sensor driver(s), actuator driver(s), mapper, planner, UI, etc.
Individually compiled, executed, and managed
Nodes are written using a ROS client library
  roscpp: C++ client library
  rospy: python client library
Nodes can publish or subscribe to a Topic
Nodes can also provide or use a Service

## Slide 8: ROS Topics
A topic is a name for a stream of messages with a defined type
  e.g., data from a laser range-finder might be sent on a topic called scan, with a message type of LaserScan
Nodes communicate with each other by publishing messages to topics
Publish/Subscribe model: 1-to-N broadcasting

## Slide 9: ROS Topics

## Slide 10: ROS Messages
Data sent between nodes.
Strictly-typed data structures for inter-node communication.
Example:
  sensor_msgs/Image

## Slide 11: ROS Services
Request/reply communication between nodes.
Synchronous inter-node transactions
Service/Client model: 1-to-1 request-response
Service roles:
  carry out remote computation
  trigger functionality / behavior
Example:
  map_server/static_map: retrieves the current grid map used by the robot for navigation

## Slide 13: ROS Basic Commands
roscore
  roscore is the first thing you should run when using ROS
  roscore will start up:
    a ROS Master
    a ROS Parameter Server
    a rosout logging node
rosnode
  Displays debugging information about ROS nodes
rostopic
  Gives information about a topic and allows to publish messages on a topic
rosmsg
  Displaying information about ROS Message types

## Slide 14: ROS Basic Commands
roslaunch
  a tool for easily launching multiple ROS nodes as well as setting parameters on the Parameter Server
rosbag
  for recording from and playing back to ROS topics
rviz
  rviz is a ROS 3D visualization tool that lets you see the world from a robot's perspective

## Slide 15: ROS and OpenCV
ROS passes images in its own sensor_msgs/Image message
cv_bridge is a ROS package that provides functions to convert between ROS sensor_msgs/Image messages and the objects used by OpenCV

## Slide 16: Synchronize Messages across all Cameras
message_filters.ApproximateTimeSynchronizer()
  Algorithms: https://wiki.ros.org/message_filters/ApproximateTime
  Example: https://gist.github.com/zxf8665905/2d09d25da823b0f7390cab83c64d631a

## Slide 17: Record Rosbag from Multiple Cameras
Run roscore to start the Master Node

## Slide 18: Record Rosbag from Multiple Cameras
Run roslaunch to start the Camera Nodes
Run rosbag to start the Camera Nodes

## Slide 19: Reference
ROS commands
  rosnode: https://wiki.ros.org/rosnode?distro=noetic
  rostopic: https://wiki.ros.org/rostopic
  rosbag: https://wiki.ros.org/rosbag?distro=noetic
  roslaunch: https://wiki.ros.org/roslaunch?distro=noetic
  cv_bridge: https://wiki.ros.org/cv_bridge
Example to use ApproximateTimeSynchronizer for message synchronization
  https://gist.github.com/zxf8665905/2d09d25da823b0f7390cab83c64d631a

## Slide 20: Thank You